## Slide 1: IHSMarkit and UT Austin CCUS GOM Data Prototype
March 2022
Michael Pyrcz
The University of Texas at Austin

## Slide 2: Operational Capability Development
‘We are the original data-driven science, we have been big data long before tech learned about big data!’
Probability and Stationarity
Kolmogorov
1930-1940s
Volume Variance in Mining
Krige
1950-1960s
Geostatistics
Mathematical Morphology
Matheron
Applications in Oil and Gas, Environmental
Journel, Verly, Deutsch
1980-1990s
>1990s
Spatial Statistics, Big Data Analytics and Machine Learning
‘We are the original data science, we have been doing it for a long time!’

## Slide 3: Summary
Fast sprint to prototype components of the proposed GeoDataAnalytics workflow for CCUS potential prediction with demonstration with IHSMarkit Gulf of Mexico data.
Goal
Provide well-documented prototypes of workflow components in Jupyter
Demonstrate codes, methods, sequential flow, diagnostics / visualizations to support implementation
Comments
Results should not be used for decision making
In sprinting forward to fast prototypes, I have made assumptions to fill gaps, for example:
Only static pore volume calculation, no effect to capture injectivity and trapping
Coordinates were not projected to North American Datum and used as original lats and longs.
Fluid types and ages were mixed in some analysis, outliers are retained

## Slide 4: The CCUS Workflow
For more information see the proposal document, UHSMarkit_UTAustin_Q1_2022_CCUS_Proposal.docx.
Main Workflow Steps
Feature Selection
Dimensionality Reduction
Feature Imputation
Feature Engineering
Workflow Outputs
While there are many intermediate outputs the main outputs are:
CO2 Storage Uncertainty Maps
CO2 Storage Risk Maps
CO2 Storage Groups
Reservoir Information (e.g., rock volume, porosity, temperature, pressure)
Regional Trend Maps
Basin Trend Maps
Spatial Distribution Debiasing
Integration of Spatial and Temporal Scale
Feature Selection
Dimensionality Reduction
Feature Imputation
Feature Engineering
CO2 Storage Capacity Proxy Model
CO2 Storage Uncertainty Maps
CO2 Storage Risk Maps
CO2 Storage Groups

## Slide 5: The Data and Data Loading
The provided data includes GOM:
Reservoir averaged features
Reservoir outlines
Codes have been developed to process the data including:
Loading all features of interest into Pandas DataFrames from ASCII comma delimited files
Extracting polygons and multipolygons from the string field of the DataFrames
Statistical analysis and diagnostics
All codes are in Python and use the most common open- source packages. I avoided use of highly specialized packages that are difficult to work with and may not be maintained. GeostatsPy (Pyrcz et al., 2022) is included
For grid-based analysis and mapping:
A reasonable 2D regular grid has been assumed for balanced computational time, coverage and resolution

## Slide 6: The Data and Data Loading
Loaded reservoir polygons in original coordinates, latitude and longitude (degrees)
Reservoir averag

## Slide 7: The Data and Data Loading
Loaded reservoir polygons in original coordinates, rasterized to the assumed 2D regular grid for mapping

## Slide 8: The Data and Data Loading
Reservoir Centroids-based DataFrame calculated:
Centroids calculated over the rasterized reservoirs
Matched with all reservoir averaged features
Areas calculated and added

## Slide 9: Debiasing Spatial Data
Spatial data debiasing with cell-based declustering:
Calculation of declustering weights
Development of flexible, diagnostic plotting functions
Inclusion of statistical weighting to means, variances and distributions

## Slide 10: Debiasing Spatial Data
Spatial data debiased reservoir scale feature distributions

## Slide 11: Spatial Data Anomaly Detection
For data cleaning, segmentation of populations for improved analysis and model accuracy:
Spatial continuity-based anomaly detection (Liu and Pyrcz, 2021).
Indicating reservoirs that are significantly different than neighboring reservoirs.
Shown with Miocene reservoirs only.

## Slide 12: Multivariate Analysis
Matrix scatter plots:
For pairwise feature evaluation to identify potential issues for feature selection, feature projection and correlation analysis.
With by-group joint distribution fits by kernel density estimation
Identification of bivariate outliers, linearity and homoscedasticity

## Slide 13: Multivariate Analysis
Matrix scatter plots
For pairwise feature evaluation to identify potential issues for feature selection, feature projection and correlation analysis.
With by-group joint distribution fits by kernel density estimation
Identification of bivariate outliers, linearity and homoscedasticity

## Slide 14: Multivariate Analysis
Conditional distributions to evaluate nonlinear, heteroscedastic relationships

## Slide 15: Feature Selection
Enhanced pairwise feature correlation analysis with partial correlation and mutual information:
Difference between partial and Pearson indicate influence of other features.
Difference between mutual and Pearson indicate influence of nonlinearity and heteroscedasticity

## Slide 16: CO2 Storage Groups
Multidimensional scaling (MDS) to project reservoirs to a lower dimensionality space:
Preserving reservoir pairwise dissimilarity while projecting from m dimensional (all predictor features) to 2D
Posting response feature, static pore volume (MMbbls) groups, low, mid and high
Natural groups in MDS space

## Slide 17: Spatial Feature Trend Models
Computational efficient trend modeling with sparse data convolution

## Slide 18: Spatial Feature Trend Models
Trend diagnostic plots to evaluate trend quality:
check for residual and trend relationships and decomposition of variance between trend and residual

## Slide 19: Static Pore Volume Modeling
Use of rasterized predictor features to calculate static pore volume maps with uncertainty:
Accounting for reservoir extent in the models
Check for relationship between reservoir average porosity and average thickness
Currently supports assumption of independence for uncertainty analysis

## Slide 20: Static Pore Volume Modeling
Calculation of 2D predictor feature spatial continuity models:
Use of variogram maps for improved visualization and diagnostics

## Slide 21: Static Pore Volume Modeling
Calculation of 2D predictor feature spatial estimates:
Includes local error variance minimized estimates and estimation variance (uncertainty)

## Slide 22: Static Pore Volume Modeling
Calculation of 2D map of static pore volume:
Local most likely estimate for by-grid column reservoir pore volume.
Extrapolation away from known reservoirs included with contour.

## Slide 23: CO2 Storage Uncertainty Maps
Local feature and static pore volume uncertainty models for any location:
No accounting for reservoir boundaries

## Slide 24: Transfer Function
Use of rasterized predictor features to calculate static pore volume maps with uncertainty:
Check for relationship between reservoir average porosity and average thickness
Currently supports assumption of independence for uncertainty analysis

## Slide 25: Static Pore Volume Modeling
Calculation of 2D uncertainty models:
Local P10, P50 and P90 static pore volume predictions for all columns

## Slide 26: Next Steps based On IHSMarkit Feedback
Coordinate transformations given the preferred projection
Integrate improved transfer function to go beyond static pore volume for oil and gas reservoirs
Addition of risk maps.
Additional feedback?
  local risk maps, filters by threshold and probability of success, distance to emitter
  add naïve histograms to declustered
  saline aquifer data

## Slide 27: Updates – Coordinate Projection
Assumed WGS84, updated areas and volumetric calculations.

## Slide 28: Updates – Declustered Distributions

## Slide 29: Updates – Declustered Distributions

## Slide 30: Updates – Add Response Feature to Correlation Analysis

## Slide 31: Updates – Trend Diagnostics

## Slide 32: Updates – Local Uncertainty with Reference Distributions

## Slide 33: Updates – Local Uncertainty with Reference Distributions

## Slide 34: Updates – Risk Maps

## Slide 35: Updates – Risk Maps

## Slide 36: Updates – Risk Maps

## Slide 37: Saline Aquifers
Fast sprint to demonstrate workflow building blocks.
Trend based Imputation and Prediction with:
robust use of statistics
uncertainty models
rapid calculations for real-time feedback
2D + 1D approach
New Steps:
dask Python package for loading and managing large datasets
1D trend displays
2D + 1D trend based imputation and pre-drill prediction

## Slide 38: Working with Big Data
dask Python package provides functionality for efficiently working with big data
10 seconds to create dask DataFrame with 235 M rows
type casted Formation Top as object
10 seconds to filtere to WILCOX Formation Tops only for 2.5 M rows
then converted to Pandas DataFrame
removed records missing NPHI for 562 k rows, 22 k without missing values, 54 unique wells
converted any records with NPHI in percent to fraction
Depth Prime is TVD with missing values set as Depth
Cleaned DataFrame preview.
Proportion of missing values in cleaned data.

## Slide 39: Debiasing Spatial Data
Spatial data debiasing with cell-based declustering:
Calculation of declustering weights
Development of flexible, diagnostic plotting functions
Inclusion of statistical weighting to means, variances and distributions
Declustering by-feature
Examples of by-feature debiasing, up to 5% correction in mean.

## Slide 40: Debiasing Spatial Data
Spatial data debiased reservoir scale feature distributions
naïve and debiased feature distributions.

## Slide 41: Multivariate Analysis
Matrix scatter plots:
For pairwise feature evaluation to identify potential issues for feature selection, feature projection and correlation analysis.
With by-group joint distribution fits by kernel density estimation
Identification of bivariate outliers, linearity and homoscedasticity

## Slide 42: Feature Selection
Enhanced pairwise feature correlation analysis with partial correlation and mutual information:
Difference between partial and Pearson indicate influence of other features.
Difference between mutual and Pearson indicate influence of nonlinearity and heteroscedasticity
Outliers are Reducing Correlation
Nonlinear Structures are Reducing Correlation

## Slide 43: CO2 Storage Groups
Multidimensional scaling (MDS) to project reservoirs to a lower dimensionality space:
Preserving reservoir pairwise dissimilarity while projecting from m dimensional (all predictor features) to 2D
Posting response feature, static pore volume (MMbbls) groups, low, mid and high
Natural groups in MDS space
To be completed. Need to apply imputation workflows first.

## Slide 44: 2D + 1D Modeling Workflow
Calculate 2D Area and 1D Vertical trends:
Combine 1D and 2D 3D.
2D Areal Trend From Well Averages
1D Vertical Trend Layer Averages
Model and Well Data
2D Trend Model
1D Trend Model
3D Trend Model
Average
over Wells
Average
over Layers

## Slide 45: Spatial Feature Trend Models
Computational efficient trend modeling with moving window conditional distributions.
1D vertical trends with uncertainty intervals
sampled conditional distributions with specified binning rate to reduce noise
applied spline curve of low order to further reduce noise and improve interpolation and extrapolation
Vertical trends by 1D moving window in depth, P40-P60 orange, P25-P75 yellow, P10-P90 grey.

## Slide 46: Spatial Feature Trend Models
Spatial Continuity Analysis
Trend and directionality detection
To be completed.
Variogram maps to detect spatial trends and continuity major and minor directions.

## Slide 47: Spatial Feature Trend Models
Computational efficient trend modeling with sparse data convolution
by-well averages
sparse data convolution for fast calculation

## Slide 48: Spatial Feature Trend Models
Trend diagnostic plots to evaluate trend quality:
check for residual and trend relationships and decomposition of variance between trend and residual

## Slide 49: Local Feature Uncertainty Models
Local feature and static pore volume uncertainty models for any location:

## Slide 50: Future Work
Impliment feature imputation and check to densify multivariate dataset to support
MDS
Predictor Feature Importance and Sensitivity
Pore Volume Calculation with Uncertainty Models